## Slide 1
GumboNodes: Exploring Sensor Networks Cheaply
Zachary Rubin (), H. Blake Skinner (hskinner@ucsc.edu) Baskin School of Engineering
University of California, Santa Cruz
Intro
Hardware
Proof of Concepts and Prototypes
The protypes sat on a breadboard ($1.20/unit). The total cost per node was $7.59 after accounting for shipping and tax.
2 Types of Nodes:
GumboTiny, the proposed hardware
GumboUno, the wireless chip attached to an Arduino Uno for data output over serial
CC2500 provided numerous hardware features. A 16 bit preamble and 2 byte checksum were added to each packet, and link quality indicator was used to determine utility of data from other nodes.
Challenges
Hardware too small to support an OS like Tiny or Contiki
Zigbee compatible transceivers too expensive
Low Packet Error Rate surprisingly difficult
  TX, RX, and Sleep
  Bad data propagates quickly.
  Multihop = bad data always ‘fresh’
Contiki
Heartbeats
Random intervals
ContikiOS Investigation: Simulation of Heartbeats vs Random Intervals
  Deciding between TX, RX, and Sleep
Built 20 GumboNodes: 18 GumboTinys and 2 GumboUnos
  Simple heartbeat
  Sleep Current: 2.5mA
  TX/RX Current: 16.mA
  Lifetime: 2.5 Days and counting!
Stuff blew
  We dropped them into a fan
Results
Future Work
Having Contiki nodes interact with real nodes
Determining a way to prevent bad data from propagating.
Want to investigate wireless sensor networks
Too Expensive per-node
  $100-150 per mote for Telos motes
  Want to evaluate more than just 1-2 nodes
Target: 20 Nodes for <$150
Atmel ATTiny85 MCU @ 1MHz
  Low Power Sleep Modes
  5 I/O pins
TI CC2500 2.4GHz Wireless Transceiver
  Low Power, Non-Zigbee
  Outputs LQI and RSSI
3v 660MAH CR2450 Battery
Simulation
Contiki the OS
Not a raft
References
Your mom
ContikiOS was used to simulate the nodes and investigate network throughput as well as overall performance between various types of communication.